## Slide 1
Road Asset Management System (RAMS) in the Kyrgyz Republic
Session 1: RAMS Introduction
Serge Cartier van Dissel
June 2021

## Slide 2: Agenda
Meeting Agenda
1. RAMS introduction What is the function of a RAMS How does a RAMS fit into the wider context of road management What are the phases of RAMS development How does Kyrgyz Republic compare to other CAREC countries
RAMS development What data has been collected in the Kyrgyz Republic What is the functionality of the database How is the collected data used for selecting and prioritizing treatments What remains to be done for the RAMS development
RAMS integration How to ensure an appropriate institutional framework for RAMS operation How to integrate the RAMS into annual planning and budgeting procedures What funding levels are required for the road sector and how can these be financed How can we develop domestic capacity to implement the planned works

## Slide 3: Road Asset Management System
Any system that is used to collect, manage and analyse road data for road planning and programming purposes
Purpose: Optimizing the level and the allocation of road funding in relation to medium- and long-term results regarding road conditions and road user costs
  Define the road network maintenance, repair and improvement needs
    Based on inventory, condition and traffic data
  Determine the required budget to address those needs
  Determine how the available budget is best allocated
    To different roads and networks (class, traffic, etc.)
    To different treatment types (maintenance, current repair, mid-term repair, capital repair)
  Based on agreed prioritization criteria
    Economic (e.g. road user costs, traffic levels)
    Social (e.g. population, minimum access)
  Predict the impact of that budget allocation
    On future road network conditions
    On future maintenance and repair costs
  Monitor the road network over time

## Slide 4: Network vs Project Planning
RAMS is a network planning tool – Limited data for all roads
  Planning for an entire (sub-)network
  Based on data collected for entire (sub-)network
  Identify best treatment approaches
  Determine budget needs and propose budget allocations
  Limited data collection to reduce costs
Different from project level planning – Detailed data for some roads
  For specific road (section)
  Much higher data requirement
  Support preparation of designs
  Determine volumes of works

## Slide 5: Benefits of a RAMS
Allows objective identification of all treatment needs and costs
  Identification of needs and future timing of treatments
  Traditional planning generally shows only part of treatment needs
  Traditional planning is generally more subjective and difficult to verify
Allows allocation of the available budget to be optimized
  Optimize impact on reducing road user costs (costs to the economy)
  Optimize impact on future road network conditions
  Traditional planning is often suboptimal – focus on fixing defects rather than preventing them
Provides basis for determining suitable budget levels
  Show the impact of different budget levels of future network conditions and road user costs (cost to the economy)
  Provides proper basis for negotiations on budget levels

## Slide 6: Costs of a RAMS
Collection of network data
  Annual collection of data for part of the network
  Cost depends on data types to be collected and collection frequency
  Survey equipment procurement/replacement and annual operation
RAMS database operation and data analysis
  Small team of dedicated staff involved in database operation and data analysis
  Resources for operation of the RAMS equipment and software
Costs of the RAMS more than compensated by increased efficiency in the use of the road sector budget
  Long-term savings in budget needs for the road network

## Slide 7: Road Asset Management System
Data management
Reporting
Data collection
Survey equipment
Data analysis
Planning module
RAMS database

## Slide 8: Road Asset Management System
Data collection
  Road data (inventory, condition, traffic, other)
  Treatment data (costs, performance, etc.)
  Missing / outdated data makes a RAMS useless
Data management (database)
  Store data and make it easily accessible
  Combine different data sets
  Prepare reports - provide statistics for the network
Data analysis (planning tool)
  Identify required budget
  Criteria for prioritization + allocation of specific budget
  Algorithms for predicting future road deterioration and user costs
May incorporate other modules
  Bridge or tunnel management system
  Contract management system
Data collection
Data management
Data analysis

## Slide 9: RAMS Integration
Institutional framework
  Resources for RAMS operation
  Procedures for RAMS operation
  Especially data collection
Planning and budgeting procedures
  RAMS integration into planning systems
  In time for budget preparation
  Used as basis for budget preparation
Financing procedures
  Influence budget levels by predicting impact on future network conditions
  Identify alternative financing options
Implementation modalities
  Capacity to implement planned works
  Shift towards mid-term repair
  Suitable contracting modalities
Institutional Framework
Implementation
Financing
Planning
Data collection
Data management
Data analysis

## Slide 10: RAMS development phases
Phase 1: Piloting
  Data collection for small part of the network
  Simple (temporary) database for data storage with limited functionality
  Data analysis using commercial software (RONET, HDM4)
  Often carried out by consultants
Phase 2: Development
  Data collection for entire road network
  Proper RAMS database with extended functionality
  Data analysis through integrated planning module or external software
  Often carried out by government (outsourced) with project consultant support
Phase 3: Integration
  Institutional framework established for RAMS operation
  RAMS forms the basis for annual and multiannual planning and budgeting
  Budget levels and allocations influenced by RAMS analysis of needs and priorities
  Domestic implementation capacity responds to new priorities (mid-term repair)

## Slide 11: RAMS status in the CAREC Region
Chart: 
| AFG | AZE | PRC | GEO | KAZ | KGZ | MON | PAK | TAJ | TKM | UZB
Phase 1: Piloting | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Phase 2: Development | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Phase 3: Integration | 1 | 1 | 1 | 1
 | AFG | AZE | PRC | GEO | KAZ | KGZ | MON | PAK | TAJ | TKM | UZB
Data collection frequency | Inter-mittent | Inter-mittent | Annual | Annual | Inter-mittent | Inter-mittent | Inter-mittent | Annual, outsourced | Starting | Starting | Inter-mittent
Data collection extent | Partial Network | Network | Network | Network | Partial Network | Partial Network | Partial Network | Network | Partial Network | Partial Network | Partial Network
Database | Being prepared | Yes | Yes | Yes | Yes | Yes | Not used | Yes | Being prepared | Limited scope | Being prepared
Data analysis | Being prepared | Inter-mittent | Most provinces | HDM4 | Being prepared | Being prepared | Not used | HDM4 | Being prepared | - | Being prepared
RAMS unit | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | - | -
RAMS influencing planning | - | Inter-mittent | Some provinces | Yes | - | - | - | Yes | - | - | -
RAMS influencing financing | - | - | - | Yes | - | - | - | Yes | - | - | -